## OMI-CS-50 e-VIEW

INTERNATIONAL

#### SINGLE PLANE GI  /  ERCP IMAGING SYSTEM

#### FLUORO and DIGITAL SPOT IMAGING

SYSTEM SPECIFICATIONS

# QTY.    CAT.NO.   DESCRIPTION

1	A-550	OP-50 X-RAY GENERATOR, R/F APPLICATION

High Frequency, 50 kW, up to 240 kHz Ripple Frequency

- kV Radiographic		40-150 kV

- mA Radiographic		10-630 mA

- kV Fluoro			40-125kV

- Pulsed Fluoro mA		16 - 80

- Pulsed Fluoro Rates		0.25 to 30.0 f/s

- Single Tube Operation

- AEC/ ABS

- 400 or 480 VAC, 3 Phase

- Dual Speed Starter

- Digital Interface

1	 B-100	ISOCENTRIC FLOOR MOUNTED I/C POSITIONER

- Motorized Vertical SID	         	            	         8  inches

- Manual Rotation of ‘I’ Section			   180 degrees

- Motorized ‘C’, LAO/ RAO with 14” I I	              ± 45 degrees

- Motorized ‘C’ Cranial / Caudal with 14” I I	      ± 30 degrees minimum

1	 B-503	System Control - Tableside or Mobile Stand Mounting.  Controls both

‘C’ Arm and Table Motions.

1	 C-500	PATIENT TABLE

- Six (6) way Motorized Tabletop - 27” wide x 84” long

Longitudinal Tabletop Travel	               16 inches

Transverse Tabletop Travel		   10 inches

Tabletop Longitudinal Tilting	          ± 12 degrees

Tabletop Lateral Tilting	          	          ± 12 degrees

- Motorized Tabletop Elevation	         32 - 42 inches

- Table Radiation Shield (ERCP)

- Radiolucent Table Pad

- Patient Restraints (3)

- Set of two (2) Arm Boards

- Rated Patient Load				500 Pounds

1	C-017	Table Radiation Shield

OMI-CS-50 E-VIEW  INTERNATIONAL			               JANUARY 1, 2007			            Page 1 of 3

QTY.      CAT.NO.     DESCRIPTION

1	 D-430	HIGH RESOLUTION IMAGE INTENSIFIER PACKAGE

- Select 14”/ 10”/ 7” Image Tube & Power Supply

- Auto Iris, I I Grid and Collision Device

2          D-505	18” Flat Panel Display for Procedures Room

2          D-505	18” Flat Panel Displays for Image Processor

1	 D-612	CEILING SUSPENSION for THREE (3) FLAT PANEL DISPLAYS

- 13’4” Ceiling Rails

1	          E-606	PRINCESTAR HIGH RESOLUTION R / F DIGITAL IMAGE PACKAGE

- Advanced Format CCD Camera - 1024 x 1024 x 12 Bit

- Integrated Auto Aperture/ Lens/ Mount

- Auto Calibration

- Image Quality Analysis/ Measurement Software

- High Speed CPU

- 80 GB Hard Drive - Stores 15,000 RAD and Fluoro Images

- Real-Time 5 Level, 13 x 13 Edge Enhancement

- Real-Time Auto-Image Optimization

- 9 Level Fluoro Noise Reduction - Pixel by Pixel Correction

- Zoom/ Pan x 2

- Annotation, Text, Line, Arrow

- Measurement Package - Length, Multi-Segment, Angle, Calibration

- Digital Shutters

- Fluoro Dynamic Range (kV and mA Tracking)

- Multi-Image Display 4 on 1 and 16 on 1

- Image Export to BMP or JPEG

- Fluoro Looping

- Static High Resolution Reference 14 Image Feature

1	 F-615	ROUND FIELD COLLIMATOR with LUNG FILTER

- Automatically collimates to selected field size

- Automatically tracks SID

1	 G-105	MGT HIGH SPEED DUAL FOCUS X-RAY TUBE with Fast Cooling

Anode

- 600,000 heat unit anode

- 12( target, 270( horns

- Rated 11/49 kW

- 0.3 - 0.8 f/s

1          G-500	QUIET STYLE HEAT EXCHANGER

- Reduces X-ray tube heat by 100,000 heat units per minute

1	 H-800	Set of System Interconnecting Cables

1  	 H-806	Pair of Low Noise High Voltage Cables, 65’

OMI-CS-50 E-VIEW  INTERNATIONAL		                                  JANUARY 1, 2007   		                       	Page 2 of 3

###### QTY.   CAT.NO.     DESCRIPTION

1 	 I-111	Electronic Rack Cabinet

1   	 I-110	CPU Electronics Enclosure

1	 Z-100	Complete Factory Pre-Staging of System

1	 Z-530	INTEGRATED FLUOROSCOPIC DOSE READOUT SYSTEM

- Displays accumulated dose per study

- Displays accumulated fluoroscopic exposure time per study

- Displays patient’s entrance dose rate

- End of study reset

Note:  Specifications subject to change without notification

OMI-CS-50 E-VIEW  INTERNATIONAL			                   JANUARY 1, 2007		      	               Page 3 of 3